JUM-X2 / JUM-X1	UNIVERSAL MILLING MACHINE

Original:

GB

Operating Instructions

JPW (Tool) AG

T鋗perlistrasse 5 CH-8117 F鋖landen Switzerland

Phone	+41 44 806 47 48

Fax	+41 44 806 47 58

www.jettools.com

M- ITASU2 / ITASU1 	2014-02

Important Safety Specification

To operators:

1．	To avoid electrical shock and harm, basic safety protection shall be enhanced when using electric tools, machines and equipments;

2．	Keep the environment around the machine clean and tidy, since a disorderly environment will bring danger;

3．	Do not install the machine in places vulnerable to rain or moisture. No flammable liquid (e.g. petroleum) is allowed near the machine;

4．	Children shall stay away from workplace;

5．	All  the  equipments of  the  machine  shall  be  equipped  with safety grounding devices to protect personal safety;

6．	Operators shall keep a clear head, do not operate when tired;

7．	Drinking and narcotics may affect one抯 judgment, so no operators with these conditions are allowed to operate;

8．	Do  not  wear  loose  clothes,  neckties  or  precious  jewels  to  avoid dangers of being caught by the moving parts.

9．	Operators shall wear hard hats to cover long hair.

10． Operators shall wear protective goggles in case that iron filings fly into the eyes.

11． During the work, operators shall remain in a correct posture and keep their balance.

Contents

Main technical parameters	厖. 4

Technical parameters Loading list

Appearance and main component diagram of JUM-X2

milling bed	厖. 6

Machine installation	厖. 7

| iv. | Driving system | 厖. 8 |
| --- | --- | --- |
| v. | Operation and maintenance | 厖. 9 |

Basic positioning Cautions before operation

Electrical operation Mechanical operation

Appendixes

| vi. | Troubleshooting | ��.12 |
| --- | --- | --- |
| vii. viii. | Circuit diagram Exploded drawing of parts | 厖.13 厖.15 |
| ix. | Part detail list | ��.16 |

Brief description

JUM-X2 / JUM-X1 Series milling bed is a small desktop lifting one, which can be switched to vertical or horizontal bed by changing the position of the power head. The vertical bed can do oblique milling by rotating the power head on the vertical plane. The two modes share one power head.

The spindle drive of JUM-X2 / JUM-X1 Series milling bed adopts infinite variable speeds.  Comparing with  the  traditional  gear drive  and pulley drive,  the synchronous pulley drive has a novel structure, low noise, stable drive and easy operation. The parts it can process have a broad range of application. It has comprehensive functions of vertical milling, horizontal milling, drilling, and boring. It is an ideal machine of family modeling, metal-processing learning and processing and repair.

(Ⅰ) Main technical parameters

Maximum drilling capacity	13 mm

Face milling capacity	30 mm

Surface milling capacity	30 mm

Maximum blade-shaped cutter diameter	63 mm

Maximum distance from the spindle face to the worktable of vertical milling bed	265mm for JUM-X2

165 mm for JUM-X1

Maximum distance from the spindle face to the worktable of horizontal milling bed	230 mm for JUM-X2

130 mm for JUM-X1

Rotating angle of the spindle carrier of vertical milling bed	�45 degrees

Taper hole of spindle	MT3

Spindle rotation speed (infinitely variable speed)	0-2500 r/ min � 5%

Size of the worktable

Size of T-slot

Lateral moving distance of the worktable

Vertical moving distance of the worktable

460�120 mm

12 mm

120 mm

300 mm

Z-directed moving distance of the worktable	205 mm for JUM-X2

105 mm for JUM-X1

Motor power

Net weight / Gross weight:

500W

95/115 kg

Packing List

| No. | Name | Specifications | Quantity |
| --- | --- | --- | --- |
| 1 | Milling bed | JUM-X2 / JUM-X1 | 1 set |
| 2 | Operation specifications |  | 1 book |
| 3 | Drill chuck and keys | B16 1~13mm | 1 unit |
| 4 | Taper-shank arbor | X20206 | 1 piece |
| 5 | Oil can |  | 1 piece |
| 6 | Inner hexagon spanner | S: 3, 4, 5, 6 | 1 in each size |
| 7 | Double-ended spanner | 5.5�7, 10�12 | 1 in each size |
| 8 | Double-ended spanner | 14�17, 21�24 | 1 in each size |
| 9 | Hook spanner | 22~26 | 1 piece |
| 10 | T-nut | X22001 | 2 |
| 11 | Gear shift lever | X1025200 | 1 |

(Ⅱ) Appearance and main component diagram

of JUM-X2 / JUM-X1 milling bed

14	4

13

7

7

6

12

8

9	2

10

5

11

4

3

1

| No. | Quantity | Name | No. | Quantity | Name |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | Base | 8 | 1 | Spindle box of vertical milling bed |
| 2 | 1 | Upright post | 9 | 2 | Locating locking block |
| 3 | 1 | Lift | 10 | 1 | Mounting holes of horizontal milling bed |
| 4 | 1 | Vertical worktable | 11 | 1 | Spindle of horizontal milling bed |
| 5 | 1 | Horizontal worktable | 12 | 1 | Junction block of horizontal milling bed |
| 6 | 1 | Ram | 13 | 1 | Locking lever |
| 7 | 1 | Components of milling head | 14 | 1 | Locking mechanism of spindle box |

(Ⅲ) Machine installation

Basic positioning

The whole machine and worktable shall be fixed with four hexagon bolts.

Continuous working period and machine accuracy must be taken into consideration. It shall be installed in the proper position to make it available to use.

The selection of installation positioning:

Rigid worktable shall be padded on a flat adjuster block.

In order to avoid the effect of high temperature on the machine, do not install the machine in sunny places.

The machine shall be installed away from dusty and wet places to avoid corrosion and rust.

Important positioning methods

1） Drill  four  positioning  holes  on  the  mounting  surface  of  the worktable.

(Notes: in terms of the installing position, hand wheels of the Y- axis shall be considered for easy rotation and operation.)

2） Adjust the machine to a horizontal position.

Use four M10 bolts to fix the worktable and the machine.

Before operation

When installation is finished, operators shall understand and grasp the basic structure, functions and controlling operations of the machine. Check whether the power source, voltage and the power supply are correct and regular.

During installation, all the clamping devices shall be fixed.

Check whether the power source and voltage are correct.

Before  using the  machine,  fill  mechanical  lubricating oil  to  the sliding surface of the machine.

Check the chucks, clamping key and fixed pin on the spindle to make them under no load.

Check whether the driving parts are regular, whether each operating handles are in right positions, whether the tool clips (drills, milling

cutters, etc.) are reliable and whether the processing parts are fixed tightly. Open the spindle box to lock the handle.

The spindle circles clockwise to start the machine.

When the machine is operating, its electrical devices shall conform to the working condition and have safety grounding devices.

During  the  operation,  notice  and  control  the  machine.  If  any irregular sign, it shall be stopped and repaired immediately.

(Ⅳ) Driving System

The driving system of the milling bed mainly consists of a synchronous pulley, a spindle bearing, a spindle and a motor, a motor synchronous pulley and a synchronous belt. The direct current motor starts power to work through synchronous pulley of motor, synchronous pulley of spindle and the spindle. The rotation speed is within the specified range of 0-2500 r/min by direct current through the infinite variable speed knob, which allows it to change its speed conveniently.

(Ⅴ)Operation and maintenance

Electrical operation

B	C

A

F G

D

E

H

A Power switch

B Speed showing plate C Overload indicator D Power indicator

E Potentiometer knob F Speed showing socket G Fuse holder

H Power cable

Move the speed-adjusting potentiometer E (equipped with a switch) anti-clockwise to �0�, and plug H into the plug base to connect to the power. At this time, the power green light D is luminous. (Note: if the yellow light C is luminous when the power is on, it indicates that the knob of potentiometer E is not pointed to 0. Each time the machine restarts, the knob E shall be pointed to 0.)

The circuit board of the machine has a function of overloaded protection. Once the drilling and milling amount is oversized, the machine will stop automatically, and the yellow light C is luminous; when it restarts, the knob E shall be pointed to 0.

Mechanical operation

The machine shall stop when installing cutters and parts.

Clean the inner hole of the spindle (Morse No. 3) and cone of the cutter. Push the cutter into the inner hole of the spindle and put the bar to tighten the cutter.

Put the part to be processed on the worktable, press it and move it horizontally and vertically to the needed position.

Loosen the locking handle of the lift and lift the worktable by swaying the handle.

Start the machine and select the rotation speed to do drilling and milling.

When milling the part, the spindle box and spindle shall be locked. And vertical, horizontal and lift gag shall be locked in case of a change size.

The installation and switch methods of vertical and horizontal milling beds

FIG. 1	FIG. 2

10	9	8	1

1	5

11	6

7

2	4	8

3

3	2	4

The normal bed is a horizontal one. When it switches into a vertical milling bed (as shown in FIG. 2), remove the Junction Block 10 and Spindle 9 and loosen Screw 4 in sequence to remove milling head components;

(As shown in FIG. 2) Install Spindle Box 11 in the installing hole behind Ram 8. (Notes: loosen Locking Handle 5 first and make the gap and hole of the locking blocks aligned), loosen Screw 4 and install Milling Head Component 1, then lock Screw 4 to align Locking Handle 5 to 0 and lock it.

After use

The power source shall be cut after finishing work. Clean the machine and the environment around it and wipe machine oil on the outside processing face to avoid rust of the surface and the influence on its use and appearance.

Gag adjustment

After a long period of operation, the gag on the worktable and saddle shall be adjusted to eliminate errors to keep the machine reliable and accurate.

Gag parts that need to be adjusted are shown below.

Horizontal gag between the worktable and the saddle.

Vertical gag between the saddle and the lift.

Adjust the gag set screw until the hand wheel is whirled easily and stably, and the worktable does not feel loose. Lock the nut on the set screw to finish the adjustment.

Troubleshooting

This part includes the most common questions and solutions of this model. No adjustment before the power is off and the motor stops running.

| Symptom | Possible reasons | Improvements |
| --- | --- | --- |
| The motor cannot start. | Does not switch on. Low voltage The motor shuts off or the connecting parts are loose. The carbon brush of the motor does not work. | Press the emergency stop switch button. Check whether the voltage is right. Check whether all the joints are loose or off. Change the carbon brush. |
| The fuse or the circuit breaker is off. | The wire or plug is short-circuited. The circuit board is short-circuited. The fuse or circuit breaker is not correct. | Check whether the insulated part of the wire or plug is damaged and replace with extension wires. Check whether the joints are loose, are faulty soldered or insulated, and change them in time. Install the right fuse of circuit breaker. |
| The motor is over- heated. | The motor is over-loaded. Air circulation in the motor is limited. | Decrease the load of the motor. Clean the motor to ensure the air circulation. |
| The hand wheels of the cross slide or feed slide is too loose. | The adjusting screw is not in its place. The hand wheel is loose. The screw components are worn or not in their positions. | Tighten the adjusting screw and fill lubricating oil on the bed. Tighten the knob of the hand wheel. Tighten all the loose knobs on the screw components. |
| The hand wheels of the cross slide or feed slide is too tight. | The adjusting screw is rusty. The adjusting screw is too tight. The worktable is dry. | Remove the screw, clean the bed and rust on pile joints, fill lubricating oil and re-tighten the screw. Loosen the screw and fill lubricating oil. Fill lubricating oil on the worktable and hand wheels. |
| The machine stops during the operation. | The drilling and milling is too deep. It uses the wrong rotation speed or feed speed during drilling and milling. The milling cutter is damaged. The motor or carbon brush does not work. The gear is damaged. | Decrease the depth of drilling and milling. Adopt right speed in reference to rotation speed and feed speed list. Change the milling cutter. Change the carbon brush or the motor. Change the gear. |
| The surface of final product is coarse. | Wrong rotation speed or feed speed. Broken or wrong milling cutter. Over-used adjusting screw | Adjust the right rotation speed or feed speed. Change the milling cutter. Tighten the screw. |
| The milling head can hardly move on the conveyor. | Dry conveyor The hand wheel of the Z-axis is too tight. There are scraps on the conveyor. | Fill lubricating oil. Adjust adjusting screws. Clean the conveyor. |
| The spindle cannot tightly clamp the milling cutter. | Wrong or mismatched milling cutter. The joint face of the spindle is damaged. | Change the milling cutter. Check and repair the joint face. |
| T-nut is hard to fix. | T-nut is damaged or wrong. T-slot on the worktable is damaged. | Change the T-nut. Change the worktable or a T-slot in good condition. |

JUM-X1-M...ITASU1.....1~230V,50Hz

JUM-X2-M...ITASU2.....1~230V,50Hz

For 230V

Parts Breakdown For JUM-X2 / JUM-X1 Univeral Milling Machine

13

| No. | Part no. | Descirption | Size | Qty. |
| --- | --- | --- | --- | --- |
| 1 | JUMX1-001 | Dust guard |  | 1 |
| 2 | JUMX1-002 | Fixing plate |  | 1 |
| 3 | JUMX1-003 | Screw | M6X8 | 4 |
| 4 | JUMX1-004 | Shield |  | 1 |
| 5 | JUMX1-005 | Screw | M4X8 | 6 |
| 6 | JUMX1-006 | Lock sleeve |  | 2 |
| 7 | JUMX1-007 | Hexagon socket head screw | M6X25 | 2 |
| 8 | JUMX1-008 | Washer |  | 6 |
| 9 | JUMX1-009 | Hexagon socket head screw | M6X16 | 2 |
| 10 | JUMX1-010 | Spindle box |  | 1 |
| 11 | JUMX1-011 | Latch segmentⅠ |  | 1 |
| 12 | JUMX1-012 | Little handle |  | 5 |
| 13 | JUMX1-013 | Locking screw | M6X50 | 1 |
| 14 | JUMX1-014 | Scale of degrees |  | 1 |
| 15 | JUMX1-015 | Rivet for name plate | 2X4 | 12 |
| 16 | JUMX1-016 | Indicator |  | 3 |
| 17 | JUMX1-017 | Latch segmentⅡ | M6X8 | 1 |
| 18 | JUMX1-018 | Column (For JUM-X1) |  | 1 |
|  | JUMX2-018 | Column (For JUM-X2) |  | 1 |
| 19 | JUMX1-019 | Ram |  | 1 |
| 20 | JUMX1-020 | Junction block of horizontal milling bed |  | 1 |
| 21 | JUMX1-021 | Blade milling cutter（optional accessory) |  | 1 |
| 22 | JUMX1-022 | washer | 10 | 3 |
| 23 | JUMX1-023 | Adjusting washer（Ⅱ） |  | 6 |
| 24 | JUMX1-024 | Bronze bushing |  | 1 |
| 25 | JUMX1-025 | Spindle |  | 1 |
| 26 | JUMX1-026 | Ram gag |  | 1 |
| 27 | JUMX1-027 | Slotted headless set screw | M6X30 | 2 |
| 28 | JUMX1-028 | Hexagon nut | M6 | 12 |
| 29 | JUMX1-029 | Junction block gag |  | 1 |
| 30 | JUMX1-030 | Cover |  | 1 |
| 31 | JUMX1-031 | Cross recessed small pan head screw | M3X6 | 15 |
| 32 | JUMX1-032 | Hexagon screw | M10X25 | 3 |
| 33 | JUMX1-033 | Hexagon nut | M14 | 1 |
| 34 | JUMX1-034 | Rolling boll shaft |  | 1 |
| 35 | JUMX1-035 | Rolling boll shaft |  | 1 |
| 36 | JUMX1-036 | Slotted round nut | M27X1.5 | 2 |
| 37 | JUMX1-037 | Circlip | 25 | 1 |
| 38 | JUMX1-038 | Slotted round nut | M20X1.5 | 2 |
| 39 | JUMX1-039 | Hexagon socket head screw | M8X25 | 1 |
| 40 | JUMX1-040 | Timing pulley |  | 1 |
| 41 | JUMX1-041 | Parallel key | 3X16 | 1 |
| 42 | JUMX1-042 | Parallel key | 5X10 | 3 |
| 43 | JUMX1-043 | Pulley box |  | 1 |
| 44 | JUMX1-044 | Washer（Ⅰ） |  | 1 |
| 45 | JUMX1-045 | Washer（Ⅱ） |  | 2 |

| No. | Part no. | Descirption | Size | Qty. |
| --- | --- | --- | --- | --- |
| 46 | JUMX1-046 | Gearbox bracket |  | 1 |
| 47 | JUMX1-047 | Dust guard |  | 1 |
| 48 | JUMX1-048 | Tension shaft |  | 1 |
| 49 | JUMX1-049 | Synchronous pulley of spindle |  | 1 |
| 50 | JUMX1-050 | Jugged synchronous belt | 1.5X100X9 | 1 |
| 51 | JUMX1-051 | Parallel key | 4X12 | 3 |
| 52 | JUMX1-052 | Top cover |  | 1 |
| 53 | JUMX1-053 | Bottom cover |  | 1 |
| 54 | JUMX1-054 | Hexagon headed bolt | M6X20 | 4 |
| 55 | JUMX1-055 | R8 spindle |  | 1 |
| 56 | JUMX1-056 | Spindle socket |  | 1 |
| 57 | JUMX1-057 | Rolling boll shaft |  | 2 |
| 58 | JUMX1-058 | Rolling boll shaft |  | 1 |
| 59 | JUMX1-059 | Tapping screw (for sheet metal) | ST2.9X9.5-C-H | 8 |
| 60 | JUMX1-060 | Base (For JUM-X1) |  | 1 |
|  | JUMX2-060 | Base (For JUM-X2) |  |  |
| 61 | JUMX1-061 | Lift |  | 1 |
| 62 | JUMX1-062 | Worktable |  | 1 |
| 63 | JUMX1-063 | Vertical gag |  | 1 |
| 64 | JUMX1-064 | Metric vertical screw nut |  | 1 |
| 65 | JUMX1-065 | Bearing base |  | 1 |
| 66 | JUMX1-066 | Left cover |  | 1 |
| 67 | JUMX1-067 | Metric vertical screw |  | 1 |
| 68 | JUMX1-068 | Thrust ball bearing | 8200 | 4 |
| 69 | JUMX1-069 | Metric dial |  | 2 |
| 70 | JUMX1-070 | Hand wheel |  | 3 |
| 71 | JUMX1-071 | Nut base (For JUM-X1) |  | 1 |
|  | JUMX2-071 | Nut base (For JUM-X2) |  |  |
| 72 | JUMX1-072 | Metric lifting nut (For JUM-X1) |  | 1 |
|  | JUMX2-072 | Metric lifting nut (For JUM-X2) |  |  |
| 73 | JUMX1-073 | Metric lifting screw (For JUM-X1) |  | 1 |
|  | JUMX2-073 | Metric lifting screw (For JUM-X2) |  |  |
| 74 | JUMX1-074 | Saddle |  | 1 |
| 75 | JUMX1-075 | Horizontal gag |  | 1 |
| 76 | JUMX1-076 | Horizontal screw base |  | 1 |
| 77 | JUMX1-077 | Metric horizontal screw nut |  | 1 |
| 78 | JUMX1-078 | Little cone gear |  | 1 |
| 79 | JUMX1-079 | Big cone gear |  | 1 |
| 80 | JUMX1-080 | Hexagon locking nut | M8 | 3 |
| 81 | JUMX1-081 | Metric horizontal screw |  | 1 |
| 82 | JUMX1-082 | Gag |  | 1 |
| 83 | JUMX1-083 | Hexagon headed bolt | M8X25 | 3 |
| 84 | JUMX1-084 | Thrust ball bearing | 8202 | 1 |
| 85 | JUMX1-085 | Cover |  | 1 |
| 86 | JUMX1-086 | Parallel key | 4X16 | 3 |
| 87 | JUMX1-087 | Damping spring |  | 3 |

| No. | Part no. | Descirption | Size | Qty. |
| --- | --- | --- | --- | --- |
| 88 | JUMX1-088 | Handle |  | 3 |
| 89 | JUMX1-089 | Slotted circular headed screw | M8X55 | 3 |
| 90 | JUMX1-090 | Hexagon nut | M8 | 3 |
| 91 | JUMX1-091 | Hexagon socket head screw | M6X14 | 11 |
| 92 | JUMX1-092 | Vertical screw bracket left socket |  | 1 |
| 93 | JUMX1-093 | Pressed-on forced filling oil cup |  | 2 |
| 94 | JUMX1-094 | Left bracket cover |  | 1 |
| 95 | JUMX1-095 | Hexagon set screw | M6X10 | 2 |
| 96 | JUMX1-096 | Metric ruler |  | 1 |
| 97 | JUMX1-097 | Hexagon set screw | M6X22 | 8 |
| 98 | JUMX1-098 | Zero label |  | 1 |
| 99 | JUMX1-099 | Hexagon socket head screw | M6X30 | 1 |
| 100 | JUMX1-100 | Hexagon socket head screw | M6X10 | 3 |
| 102 | JUMX1-102 | Locking nut |  | 1 |
| 103 | JUMX1-103 | Cross slot sunk screw | M3X6 | 5 |
| 104 | JUMX1-104 | Footing adjusting screw |  | 4 |
| 105 | JUMX1-105 | Hexagon nut | M12 | 4 |
| 106 | JUMX1-106 | Lifting axis |  | 1 |
| 107 | JUMX1-107 | Bearing base |  | 1 |
| 108 | JUMX1-108 | Hexagon socket head screw | M4X14 | 3 |
| 109 | JUMX1-109 | Slotted set screw with cone point | M5X8 | 2 |
| 110 | JUMX1-110 | Metric dial |  | 1 |
| 111 | JUMX1-111 | Slotted headless set screw | M6X16 | 2 |
| 112 | JUMX1-112 | Yellow luminous tube with fixed base |  | 1 |
| 113 | JUMX1-113 | Magnetic switch |  | 1 |
| 114 | JUMX1-114 | Green light |  | 1 |
| 115 | JUMX1-115 | Cross recessed small pan head screw | M5X8 | 3 |
| 116 | JUMX1-116 | Fuse holder |  | 1 |
| 117 | JUMX1-117 | Potentiometer knob |  | 1 |
| 118 | JUMX1-118 | Cross recessed small pan head screw | M4X12 | 2 |
| 119 | JUMX1-119 | Hexagon nut | M4 | 2 |
| 120 | JUMX1-120 | Brushless DC Motor | 500W | 1 |
| 121 | JUMX1-121 | Spring washer | 6 | 1 |
| 122 | JUMX1-122 | PC board box |  | 1 |
| 123 | JUMX1-123 | Switch box |  | 1 |
| 124 | JUMX1-124 | Insert 1 |  | 1 |
| 125 | JUMX1-125 | Insert 2 |  | 1 |
| 126 | JUMX1-126 | Air joint |  | 1 |
| 127 | JUMX1-127 | Switch label |  | 1 |
| 128 | JUMX1-128 | Pendant control |  | 1 |
| 129 | JUMX1-129 | Filter |  | 1 |
| 130 | JUMX1-130 | Hose fitting |  | 3 |
| 131 | JUMX1-131 | PC board |  | 1 |
| 132 | JUMX1-132 | Screw | M4X16 | 2 |
| 133 | JUMX1-133 | Screw | M4X16 | 4 |
| 134 | JUMX1-134 | Elastic ring | M4 | 4 |

| No. | Part no. | Descirption | Size | Qty. |
| --- | --- | --- | --- | --- |
| 135 | JUMX1-135 | Tapping screw (for sheet metal) | ST4.2X9.5-C-H | 8 |
| 136 | JUMX1-136 | Small PC board |  | 1 |
| 137 | JUMX1-137 | PC board box |  | 1 |
| 138 | JUMX1-138 | Switch box cover |  | 1 |
| 139 | JUMX1-139 | Plastic tube |  | 1 |
| 140 | JUMX1-140 | Standard power wire |  | 1 |
| 141 | JUMX1-141 | Pin | B4x8 | 1 |
| 142 | JUMX1-142 | Connecting plate |  | 1 |
| 143 | JUMX1-143 | Plastic tube |  | 1 |
| 144 | JUMX2-144 | Lock ring |  | 1 |
| 145 | JUMX2-145 | Screw | M5x8 | 4 |
| 146 | JUMX2-146 | Washer |  | 1 |
| 147 | JUMX2-147 | Pin | 2x6 | 1 |
| 150 | JUMX2-150 | Emergency stop button |  | 1 |